## Slide 1: Project 1.6: Distributed Robotic Beamforming
ArtIAMAS Cooperative Agreement
Quarterly review meeting on November 16, 2022
Kushal Chakrabarti, Amrit Bedi, Nikhil Chopra (UMD, PI)
Fikadu Dagefu (ARL), Jeffrey Twigg (ARL)

## Slide 2: Distributed Beamforming
Creates coherent signal using multiple antennas
Directional, Controlled Pattern
  Covert Comms
  Targeted Jamming
  Radar
Electronically steerable
Gain is N^2
5 Element Array @2W
= 1 50W Tx
Phase Controller
Coherent
Phase Front
N-element Phased Array
Distributed
Across
Robots
Objective: Wireless Communication in Presence of Near-peer Adversaries
Increasing Operational Tempo of Future Battles (Requires Autonomy)
Reliability in Complex Environments (e.g., Dense Urban, Indoors, Forests)
Inspiration: Phased Antenna Array
Distributed Robotic Beamforming
  Distributed, resilient to single-agent failure
  Agile, composed of evolving robot swarm
  AI to adapt to environment and near-peer adversary

## Slide 3
Our Contributions (since Dec 21 start)
  proposed a novel algorithm: Iteratively Pre-conditioned Gradient-descent for Distributed Beamforming (IPG-DB)
  significantly faster than the gradient-descent (GD) based methods
  does not rely on receiver feedbacks
  does not assume channel fading parameters: robustness to channel noise
  Tested on complex simulation frameworks created by ARL.
  experimentally compared with 1-bit feedback approach at ARL

## Slide 4
Empirical Results: LA Urban Environment
# beamforming agents:
# receivers:
synchronized carrier frequency :
channel data only used for testing the performance of IPG-DB
Physics based simulations using EM.Cube (ARL Data)
A section of Los Angeles
3D CAD model

## Slide 5
Empirical Results: LA Urban Environment

## Slide 6
Empirical Results: Boston Urban Environment
# Tx:
frequency: GHz
position in meters

## Slide 7
Empirical Results: Boston Urban Environment
Verified by Physics-based simulations using EM.CUBE (ARL Data)
RSS at adversary

## Slide 8
Indoor Experiments at ARL
Rx
Tx
4 different Rx position
6 dB – 1-bit feedback
6 dB in ¾ cases, 4 dB in ¼ case – IPG-DB w/o feedback
40 MHz

## Slide 9: Results Obtained and Expected Future Outcomes
Kushal Chakrabarti, Amrit S. Bedi, Fikadu T. Dagefu, Jeffrey N. Twigg, and Nikhil Chopra. Fast distributed beamforming without Receiver Feedback. In 56th Annual Asilomar Conference on Signals, Systems, and Computers. 2022.
  proposed a novel algorithm: Iteratively Pre-conditioned Gradient-descent for Distributed Beamforming (IPG-DB)
  significantly faster than the gradient-descent (GD) based methods
  does not rely on receiver feedbacks
  does not assume channel fading parameters: robustness to channel noise
  Tested on complex simulation frameworks created by ARL.
  experimentally compared with 1-bit feedback approach at ARL
  Moving receiver scenario and transmitter framework is under development