## Slide 1: Project 1.6 Distributed Robotic Beamforming
Kushal Chakrabarti, Manik Kumar, Amrit Bedi, Nikhil Chopra (UMD, PI)
Jeffrey Twigg (ARL), Fikadu Dagefu (ARL),
ArtIAMAS Cooperative Agreement
Annual Review

## Slide 2: Distributed Beamforming
Creates coherent signal using multiple antennas
Directional, Controlled Pattern
  Covert Comms
  Targeted Jamming
  Radar
Electronically steerable
Gain is N^2
5 Element Array @2W
= 1 50W Tx
Phase Controller
Coherent
Phase Front
N-element Phased Array
Distributed
Across
Robots
Objective: Wireless Communication in Presence of Near-peer Adversaries
Increasing Operational Tempo of Future Battles (Requires Autonomy)
Reliability in Complex Environments (e.g., Dense Urban, Indoors, Forests)
Inspiration: Phased Antenna Array
Distributed Robotic Beamforming
  Distributed, resilient to single-agent failure
  Agile, composed of evolving robot swarm
  AI to adapt to environment and near-peer adversary

## Slide 3: Controlling Covert Directional Communication

## Slide 4: Year 2 Anticipated results and expected joint outcomes
Task | Results/Outcomes in Collaboration with ARL
Task 1.6.1 Fundamental limits on desired pattern generation | Characterize constructively the tradeoff between generating an arbitrary far-field radiation pattern and number of deployed robotic systems
Task 1.6.2 Efficient Reinforcement learning for array control | Develop efficient novel policy gradient based RL algorithms to solve the problem of distributed beamforming

## Slide 5
Problem Formulation: Notation
beamforming agents:
receivers:
location of agent :
location of receiver :
desired array factor amplitude at receiver :
distance between agent and receiver :
excitation signal amplitude and phase of agent :
synchronized carrier frequency :
wavenumber: Hz/m

## Slide 6
Problem Formulation
constructed array factor at receiver :
unknown multipath fading
control parameters
weightage for receiver :

## Slide 7
Performance Measures of a Beamforming Approach
open-loop or closed-loop
  feedback required?
  unlikely to get feedback from null receivers
guarantee convergence
  algorithm converges? (future work)
  exact solution exists?
  how many transmitting agents? (ongoing work)
rate of convergence
  smaller number of iterations
  characterize number of iterations (future work)
robustness
  unknown channel parameters
  receiver locations not precise (future work)
directivity
  spread of combined signal in other directions? (future work)
node placement and node selection
  optimize position and the number of active agents (future work)

## Slide 8
Comparison with Related Works
Prior Works | Our Work
objective: maximizing gain or steering nulls at specific locations | objective: beampattern matching advantages: precise control over power at multiple locations, inherent beamforming and nullforming in constructive manner, can include additional constraints (limited transmit power, derivative constraints)
utilize receiver feedbacks | does not require receiver feedbacks
sparse beamforming, mobile agents | fixed number of agents, stationary agents
channel model-free, probabilistic channel prediction for minimizing power | feedback-free, objective: beampattern matching
receiver feedback-free | does not assume LOS channels

## Slide 9
Our contributions
  proposed a novel algorithm: Iteratively Pre-conditioned Gradient-descent for Distributed Beamforming (IPG-DB)
  significantly faster than the gradient-descent (GD) based method in [1]
  does not rely on receiver feedbacks
  does not assume channel fading parameters: robustness to channel noise
  can be incorporated in alternate optimization framework for position, sparsity, and excitation in [1], [2]: replace slower GD with faster IPG-DB
[1] Jemin George, Anjaly Parayil, Cemal Tugrul Yilmaz, Bethany L Allik, He Bai, and Aranya Chakrabortty. Multi-agent coordination for distributed transmit beamforming. In 2020 American Control Conference (ACC), pages 144–149. IEEE, 2020.
[2] Anjaly Parayil, Amrit Singh Bedi, and Alec Koppel. Joint position and beamforming control via alternating nonlinear least-squares with a hierarchical gamma prior. In 2021 American Control Conference (ACC), pages 3513–3518. IEEE, 2021.

## Slide 10
Proposed Settings of Beamforming Agents
server-agent based setting
  agents communicate with server
  no peer-to-peer communication
what is a server?
  can be an auxiliary node, located close to the agents
  can exchange information with the agents
  can process information
  need not know the beamforming problem
server
target Rx
null Rx

## Slide 11
Algorithm Description: IPG-DB
agent : , server:
, ,
server broadcasts to each agent:
,
-th row of
: Hessian, locally computed
, ,
,,
For each iteration :
at each agent
agent to server
at each agent
server to each agent
at server

## Slide 12
Empirical Results: Synthetic Data
# beamforming agents:
# receivers:
location of receivers: , uniform in
synchronized carrier frequency :
unknown i.i.d. Rayleigh fading
(IPG-DB)
(GD)

## Slide 13
Empirical Results: Synthetic Data
(uniform weights)
(nonuniform weights)
GD
IPG-DB
IPG-DB

## Slide 14
Empirical Results: LA Urban Environment
# beamforming agents:
# receivers:
synchronized carrier frequency :
channel data only used for testing the performance of IPG-DB

## Slide 15
Empirical Results: LA Urban Environment
IPG-DB

## Slide 16
Summary
  multi-agent beamforming problem
  objective: autonomously optimize excitation amplitude and phase to match desired beampattern, including target beams and nulls
  proposed IPG-DB
  robust to conditioning of the optimization problem and channel uncertainties
  demonstrated to reach a satisfactory neighborhood of the desired pattern faster than classical GD
  future work: estimate channel condition and incorporate in IPG-DB
  future work: optimize penalty weights
Work submitted to: Kushal Chakrabarti, Amrit S. Bedi, Fikadu T. Dagefu, Jeffrey N. Twigg, and Nikhil Chopra. Fast distributed beamforming without Receiver Feedback. In 2016 56th Annual Asilomar Conference on Signals, Systems, and Computers. 2022. (under review)