## Slide 1: Highly Interpretable Graph NNs for Real World Multi-Agent Systems
Alex Beyer
Department of Mechanical Engineering
University of Maryland
abeyer@umd.edu

## Slide 2: Why Study Multi-Agent Systems?
Multi-Agent (MA) Systems are collections of agents that solve complex problems via coordinated action
  Studying these systems also gives insights on emergent group behaviors
MA Systems are all around us!
  Self Driving Cars
  Logistics Networks
  Site/Project Monitoring[1]
Video: openai.com/research/emergent-tool-use
Notes: We’ve seen single agent systems be applied to real world problems with great results, but many problems are too complicated to be tackled by single robots – these problems typically require groups of agents acting in a coordinated way to solve well (or at all, in some cases)
As humans we are surrounded by MA systems all the time, even if we don’t realize it: self driving cars and logistics networks are two great examples
Studying MA Systems also gives very powerful insights in group dynamics and emergent behaviors, something which has been leveraged a lot recently to explore the dynamics of project teams

## Slide 3: Real-World Requirements for MA Systems
Requirement | Definition
Performance | Algorithms must be capable of accurately performing the given task
Interpretability | Algorithms must be able to provide human understandable rationale for actions taken, ideally allowing designers to step through the logic used
Fault Tolerance | MA Systems should maintain performance and safety even as communication quality varies or agents cease functioning
Extensibility | Algorithms should account minor changes in the problem (such as number of agents or changes in constraints) without much work
Transferability | Ideally, a MA framework should be able to handle a variety of problems
Definitions based on the work of [7-9]
Notes: In general, we can identify 5 main qualities a MA system should have to allow it to function well in real world human environments:
First and most critically, a system must be capable of performing its assigned task accurately and consistently – this issue is well understood, with a variety of groups demonstrating high performance MA algorithms for many tasks
Second, it’s important for safety reasons that we can understand what the system is doing and why. This allows designers to take preventative steps to stop unsafe behavior and diagnose faults after the fact
Equally as important is the idea of Fault Tolerance – that real world effects like varying communication quality and damage to individual agents should not seriously compromise the algorithms performance
An ideal MA algorithm should also function well both as the parameters of it’s problem are changed (like # agents or specific constraints) and be applicable to multiple tasks without significant rebuilding

## Slide 4: State of the Art for MA Systems
Two main approaches:
  Expert Designed, Model Based Control
  Multi-Agent Reinforcement Learning (MARL)
    Often makes use of Deep Reinforcement Learning (DRL)
G
+
+
H
Notes: With all that said, there are two main approached to solving MA coordination problems:
-Expert Designed, Model Based Controllers which use system dynamics to derive control laws that generate the desired behavior
-Data Driven Multi-Agent Reinforcement Learning, where the agents learn how to achieve a certain goal through interactions with their environments. This approach typically makes use of Deep Reinforcement Learning, a concept we’ll discuss more later
Remove lower half and get a nice picture?
There are other major considerations to this process like the degree to which centralized processing is used to aid the system or heterogeneity of agents, but these end up
Explain DRL here and say we don’t have time to go much into depth – uses ANNs to solve problems involving high dimensional data with complicated rules governing outputs, its great for solving complex problems because it requires comparatively little engineering of its features but the high dimensionality of the network and sheer number of operations involved make it difficult to interpret

## Slide 5: Model Based Control
Uses models of system dynamics to derive optimal control laws
  Provides robust guarantees of system behavior
Many recent attempts are Constraint-Driven, having been demonstrated for
  Collision free navigation via Barrier Functions[2]
  Platooning of vehicles on highways[3]
  Predator avoidance and emergent flocking[4]
Notes: The first approach I want to touch on is traditionally designed model based controllers.
As mentioned before, these rely on modeling system dynamics in an attempt to derive a control law – there are many approaches to this but one of the main focuses as of late has been on constraint driven optimal control where desired behaviors are posed as system constraints
This is an approach which been validated on a number of scenarios, from collision free navigation via Barrier Functions and Predator Avoidance to Vehicle Platooning on highways

## Slide 6: Example: Safety Barrier Certificates
Implements Centralized & Decentralized methods of preventing collision between moving agents as functions of agent accelerations
t = 0
t = 2538
t = 5000
Notes: See sec 4 for relevant eqns to include

## Slide 7: Example: Safety Barrier Certificates
Also investigates the problem of deadlock in these systems, where control laws lead to system states which can’t resolve absent extra logic
Type I
Type II
Type III

## Slide 8: Example: Predator Avoidance and Flocking[4]
Builds a Finite State Machine capable of producing emergent safety behaviors like maintaining minimum distance
Optimizes a single objective function subject to multiple constraints
[4], video from:
sites.google.com/view/ud-ids-lab/cdflock

## Slide 9: Multi-Agent Reinforcement Learning
Many algorithms used such as:
  Decentralized Partly Observable Markov Decision Processes(Dec-POMDPs)[6]
  Graph Neural Networks (GNNs)[5]
  Decentralized Asynchronous Advantage Actor-Critic (A3C)[6]
  Evolutionary Algorithms
Also need to consider:
  Centralized vs. Decentralized Learning
  Communication Strategy
  Problem Decomposition
Notes: The other main approach we’ll look at it Multi-Agent Reinforcement Learning (MARL)
This is a particularly rich subfield of Reinforcement Learning which has seen an explosion of interest in the past few years, with implementations using and combining many different RL frameworks
Remove the 2nd part and get a picture?

## Slide 10: Multi-Agent Reinforcement Learning
Many algorithms used such as:
  Decentralized Partly Observable Markov Decision Processes(Dec-POMDPs)[6]
  Graph Neural Networks (GNNs)[5]
  Decentralized Asynchronous Advantage Actor-Critic (A3C)[6]
  Evolutionary Algorithms
Also need to consider:
  Centralized vs. Decentralized Learning
  Communication Strategy
  Problem Decomposition
Notes: However, one method has stood out amongst the rest – Graph Neural Networks. Approaches based on GNNs have repeatedly been demonstrated to have incredibly desirable qualities for the control of MA systems, but what are they exactly?
Backup slide exists for extra considerations

## Slide 11: Intro to Graphs and Graph Theory
Let a graph where V is the set of nodes representing agents and E is the set of edges capturing relations between them
System information can be encoded as node features or edge features
2
3
1
4
}
See [10] for full explanation
Notes: First we need to discuss what a Graph is – these aren’t the type of graphs you’re familiar with from [school/MATLAB], but rather ways of capturing information and relationships. For our purposes, we can define a graph as a set G of vertices V corresponding to each agent and a set of edges E storing relational information. Both edges and nodes are capable of having feature vectors, which are just ways of associating certain types of data to them.
Below, we can see an example of translating a MA system into a graph. N this case every agent is capable of communication with every other agent, so every node is connected, which isn’t necessarily true for every system.

## Slide 12: Intro to Graph Neural Networks
Message Passing Neural Networks (MPNNs) are one common structure for these networks
  Nodes can pass messages to other nodes within their neighborhood with a single update being expressed as
  and are the update and message functions
  is an aggregation operator acting on neighborhood n
    For MA systems this operator is usually related to agents action spaces
See [10] for full explanation
2
3
1
4
5
Neighborhood
Notes: Now we have a notion of a graph we can begin to apply RL theory to them. GNNs were originally conceived around 2005 with little progress being made until 2017 when Kipf et al presented the first Graph Convolutional Networks, leading to the field growing into what it is today. One of the most common structures for GNNs is something called a Message Passing Network (MPNN) which allows nodes within the same neighborhood to send “messages” to one another based on their respective node and edge features. In general, a single layer of an MPNN can be expressed as an update function φ which takes in the nodes current features and an aggregated message from all nodes within the same neighborhood, which is then used to update the relevant features. By convention, the neighborhood of a node is defined as itself and any nodes one edge away.
There is incredibly rich theory behind how exactly these layers function which I don’t have time to explain fully, but reference 10 is an excellent primer on the topic.

## Slide 13: Example: Decentralized GNN based Exploration[5]
Achieves scalable communication schemes via Graph Attention Networks (GATs)
  Uses GNNs to teach the model what information to base decisions off as a function of agent spacing and relevancy
Notes: Dmeonstrates that the hierarchichal graph recurrent network (HGRN) and its actor-critic version significantly oupreform every other benchmarked algorithm in this application
GRU is gated recurrent unit, used to store valuable information long term

## Slide 14: MARL Vs. Model Based Control
Both methods have advantages
  Both are highly performant and can be fault tolerant
  Model-Based Control is readily interpretable
  MARL is highly extensible and transferable
However, there are also inherent drawbacks
  Use of DRL for MARL approaches makes interpretability difficult
  Classical Control Design leads to solutions which often transfer and can extend poorly
Notes: So far we’ve laid out two main approaches, but does either one offer a distinct advantage?
Both methods have been demonstrated to be highly performant and tolerant to faults
Model Based Controllers are very easy to interpret due to them having been designed by a human who understands all the involved parts, but they often lack transferability and extensibility, with changes in underlying dynamics and constraints requiring controls to be rederived – a difficult and time consuming process
MARL, by contrast, is incredibly extensible and transferable, only requiring a clear definition of the objective and training time in most cases. However the use of deep learning methods severely hampers interpretability by obfuscating what the network is actually doing to process an input into an output
The study of Interpretability for deep learning has been very active over the past few years, owing to a surge in the number of RL based systems applied in the real world – what if we can apply ideas from those studies to our MA problem?

## Slide 15: Model Interpretability - Dimensions
Based on work of [7,8,11]
Many metrics are difficult to quantify and there’s no definitive set!
Requirement | Definition
Transparency | Choosing model representations which have well understood properties and intuitive representation of different features
Simulatability | The ability to break a model into subsystems with understandable inputs and outputs
Decomposability | Understanding the way model components process data
Consistency | Similar inputs should lead to similar outputs
Notes: In general, I see Interpretability coming from 4 different qualities of a model:
A good model is transparent; it has well understood properties and represents data in a way humans can understand
Being able to simulate a model as a collection of simpler subsystems is also important, as well as being able to understand how all the parts of that decomposition function. Taken together, this allows designers to deconstruct complicated deep learning models into simple parts to better understand the input-output relationship.
Finally, a good model ought to be consistent; small variations in input should lead to small variations in output
Two things are also worth noting with this: these metrics are largely qualitative and theres no one universal agreed upon set, this is the set of them I’ve found the most intuitive and useful
Saliency
Identifying why a given input maps to a given output

## Slide 16: MARL Interpretability – State of the Art
Many methods have been used such as
  Imitation Learning of Proxy Models[12]
  Example Based Explanations[5,11]
  Specific Model and Objective Design[6,11]
GNNs offer two main advantages for Decentralized MA Systems
  Transparent Representations of Data[13]
  Easy to Decentralize[14]
2
3
1
4
4
Notes: Like I said before, a number of groups have been focused on this problem as of late, coming up with clever ideas like training secondary interpreter models to help give human interpretable reasoning for what a deep learning model is doing.
Where GNNs excel in this regard is their ability to offer both transparent, understandable representations of data and the fact that their structure (particularly for MPNNs) is readily decentralizeable
Add some kind of diagram to show the decentralizeability?

## Slide 17: Highly Interpretable Graph NNs for Safe Real World Multi-Agent Systems
Problem: MARL approaches lack the interpretability needed for safe implementation in real world human environment
Motivation: Interpretability and safety are intrinsically connected; a safe system is an interpretable one and designers can’t guarantee the safety of uninterpretable systems
Goal: Demonstrate an ability to consistently interpret the behaviors of systems governed by GNNs
Notes: One clear gap in the current research is that MARL methods have been proven to have a lot of desirable qualities, but at the moment a lack of interpretability makes safely implementing these systems in real world human environments very difficult
My proposal is to build on progress made towards interpreting reinforcement learning more generally to develop a specific framework to aid in interpretation of GNNs for MA applications.

## Slide 18: Highly Interpretable Graph NNs for Safe Real World Multi-Agent Systems - Approach
Equipment
  Fleet of Unmanned Vehicles with communications and processing hardware
  Unmanned drones with similar hardware for heterogeneity tests
Proposed GNN Application
  Coordinating Inter-Agent Communication for Pathfinding in Partially Observable Environments
Agents are equipped with necessary low-level controllers to facilitate motion
Notes: The equipment needed for this project are a fleet of heterogenous unmanned agents with the hardware required to enable communication and data processing
The particular task I’m interested in exploring is pathfinding in partially observable real world environments. This is a very difficult coordination task owing to the environments being unstructured and possibly dynamic – it is also a task that GNNs have demonstrated abilities to solve, albeit with many current attempts doing so in highly controlled lab environments where the lack of interpretability matters less. In keeping with the way many groups have attempted this problem, GNNs will be used to facilitate communication and coordination between the agents, wile the agents themselves are equipped with low-level controllers to facilitate motion.
Communication coordination is one of the more common applications of GNNs for MARL

## Slide 19: Highly Interpretable Graph NNs for Safe Real World Multi-Agent Systems - Timeline
Year 1, Q1-2
Develop and verify interpretability metrics
Year 1, Q3-4
Deployment in unstructured but controlled real world settings
Year 2
Extend to more realistic, totally unstructured human environments
Tests in simulation and structured lab environments
Comparison against existing state-of-the-art metrics
Rigorously verify that interpretability is maintained in more complex environments
Begin controlled Human-Robot interaction tests to ensure safety and robustness of metrics
Slowly allow more uncontrolled interactions to test model limits
Develop robust, interpretable model failsafes
Ensure all failsafes work as intended
Recheck all failsafes before allowing for more interaction between humans and agents
Apply metrics to real world heterogenous systems
Review of relevant literature to identify state of the art GNN architectures and current best methods for improving DRL and NN Interpretability
Develop frameworks for Centralized Training with Decentralized Execution (CTDE) and Decentralized Training and Execution (DTDE)
Reverify performance in CTDE and DTDE regimes
Notes: The proposed project will be split into three phases over two years:
Phase 1 will take 6 months and be focused on understanding the state of the art for RL interpretability and extending it to the kind of GNN used in this problem, with the aim of creating a set of metrics which allow for clear interpretations of model behavior. As a part of this, a set of model failsafes will be implemented to ensure that the system not only acts safely, but it able to do so in a way a human can understand.
Phase 2 occurs in the latter half of the first year, being largely focused on application to unstructured environments outside of lab while taking care to avoid uncontrolled interaction between agents and humans while the overall safety of the model is ensured. During this phase controlled HRI will be allowed to verify the work to date.
Finally, phase 3 will take the 2nd year of the project and revolve around scaling up to real world, unstructured human environments. At this stage the focus is primarily on ensuring robustness of both metrics and failsafes in the kind of environment this research would be applied to in the real world.

## Slide 20: Conclusions

## Slide 21: References
[1] L. Xiang, Y. Tan, G. Shen, and X. Jin, “Applications of multi-agent systems from the perspective of construction management: A literature review,” Eng. Constr. Archit. Manag., vol. 29, no. 9, pp. 3288–3310, Nov. 2022, doi: 10.1108/ECAM-01-2021-0038.
[2] L. Wang, A. D. Ames, and M. Egerstedt, “Safety Barrier Certificates for Collisions-Free Multirobot Systems,” IEEE Trans. Robot., vol. 33, no. 3, pp. 661–674, Jun. 2017, doi: 10.1109/TRO.2017.2659727.
[3] L. E. Beaver and A. A. Malikopoulos, “Constraint-Driven Optimal Control of Multi-Agent Systems: A Highway Platooning Case Study,” IEEE Control Syst. Lett., vol. 6, pp. 1754–1759, 2022, doi: 10.1109/LCSYS.2021.3133801.
[4] L. E. Beaver and A. A. Malikopoulos, “Constraint-Driven Optimal Control for Emergent Swarming and Predator Avoidance.” arXiv, Mar. 21, 2022. Accessed: Mar. 02, 2023. [Online]. Available: http://arxiv.org/abs/2203.11057
[5] Z. Ye, X. Jiang, G. Song, and B. Yang, “Soft Hierarchical Graph Recurrent Networks for Many-Agent Partially Observable Environments.” arXiv, Sep. 05, 2021. Accessed: Mar. 03, 2023. [Online]. Available: http://arxiv.org/abs/2109.02032
[6] G. Sartoretti, W. Paivine, Y. Shi, Y. Wu, and H. Choset, “Distributed Learning of Decentralized Control Policies for Articulated Mobile Robots,” IEEE Trans. Robot., vol. 35, no. 5, pp. 1109–1122, Oct. 2019, doi: 10.1109/TRO.2019.2922493.
[7] C. Glanois et al., “A Survey on Interpretable Reinforcement Learning.” arXiv, Feb. 24, 2022. Accessed: Mar. 02, 2023. [Online]. Available: http://arxiv.org/abs/2112.13112
[8] F.-L. Fan, J. Xiong, M. Li, and G. Wang, “On Interpretability of Artificial Neural Networks: A Survey,” IEEE Trans. Radiat. Plasma Med. Sci., vol. 5, no. 6, pp. 741–760, Nov. 2021, doi: 10.1109/TRPMS.2021.3066428.
[9] M. Dorigo, G. Theraulaz, and V. Trianni, “Reflections on the future of swarm robotics,” Sci. Robot., vol. 5, no. 49, p. eabe4385, Dec. 2020, doi: 10.1126/scirobotics.abe4385.
[10] M. M. Bronstein, J. Bruna, T. Cohen, and P. Veličković, “Geometric Deep Learning: Grids, Groups, Graphs, Geodesics, and Gauges.” arXiv, May 02, 2021. Accessed: Mar. 07, 2023. [Online]. Available: http://arxiv.org/abs/2104.13478
[11] Y. Zhang, P. Tiňo, A. Leonardis, and K. Tang, “A Survey on Neural Network Interpretability,” IEEE Trans. Emerg. Top. Comput. Intell., vol. 5, no. 5, pp. 726–742, Oct. 2021, doi: 10.1109/TETCI.2021.3100641.
[12] J. Blumenkamp and A. Prorok, “The Emergence of Adversarial Communication in Multi-Agent Reinforcement Learning”.
[13] J. Sheng et al., “Learning structured communication for multi-agent reinforcement learning,” Auton. Agents Multi-Agent Syst., vol. 36, no. 2, p. 50, Oct. 2022, doi: 10.1007/s10458-022-09580-8.
[14] J. Blumenkamp, S. Morad, J. Gielis, Q. Li, and A. Prorok, “A Framework for Real-World Multi-Robot Systems Running Decentralized GNN-Based Policies,” in 2022 International Conference on Robotics and Automation (ICRA), Philadelphia, PA, USA, May 2022, pp. 8772–8778. doi: 10.1109/ICRA46639.2022.9811744.
tinyurl.com/ABQERefs

## Slide 22: Model Interpretability – Taxonomy[11]

## Slide 23: Agent Heterogeneity & GNNs
Based on work of [7,8,11]
Often useful for MA systems to have multiple agent types:
  Drones & Ground Vehicles for Search and Rescue
  Long & Short Range Logistics Robots
Allows for flexibility in how problems are solved at the cost of complexity[15]
GNNs account for this in a few ways, depending on implementation:
  Feature Vectors and Action Spaces of different lengths
  Parameter Initalizations

## Slide 24: MARL Structure Considerations
Based on work of [7,8,11]
Centralization vs Decentralization
  Centralized Training, Decentralized Execution (CTDE)
  Decentralized Training, Decentralized Execution (DTDE)
Heterogeneity
  Agents with different abilities often improve overall performance
Problem Decomposition
  Global vs Local Objectives
  Agent State Observability
  Information Security

## Slide 25: Example: Interpretability for Decentralized GNN based Exploration[5]
Achieves a level of interpretability by using example cases
  In this example the attention component of the HGRN is studied as a mobile agent moves between two fixed agents – the GNN begins to pay attention once the agents are close enough for communication to occur without significant loss
Notes: Dmeonstrates that the hierarchichal graph recurrent network (HGRN) and its actor-critic version significantly oupreform every other benchmarked algorithm in this application