## Slide 1
Distributed Beamforming Problem
Problem: beampattern matching
  to match the desired beam and null values at multiple receiver locations
  need not consider separate problems for beam and null
  receiver locations can change over time
  channel can change over time

## Slide 2
Approach: Optimization
coefficient perturbation method
  optimization variables: beamforming phase and amplitude of each agent
  agents’ locations are fixed
  minimize the sum-of-squares error between the desired beampattern and formed beampattern at the receiver locations
  non-convex problem
node perturbation method
  node placement: select the best position of each agent
  node selection: select a subset of nodes based on their positions and beamforming coefficients
  additional variables: position of agents, active agents

## Slide 3
Performance Measures
open-loop or closed-loop
  do the agents need feedback from the beam receivers and null receivers?
guarantee convergence to a local or global optimum solution
  does the algorithm converge for arbitrary initialization?
rate of convergence
  how many iterations are required to get a close enough solution?
what is considered as close enough?
  measure the gap in dB
robustness
  channel parameters may not be known precisely
  channel noise, measurement noise

## Slide 4
Proposed Setting
server-agent based setting
  agents can communicate with a common server
  no peer-to-peer communication
what is a server?
  can exchange information with the agents
  can process information (addition, multiplication, etc. basic operations)
  need not know the beamforming coefficients, agents’ and receivers’ locations, desired beam and null values

## Slide 5
Proposed Algorithm: IPG
works in server-agent settings
open-loop or closed-loop
  does not require feedback from the receivers
assumes channel information
  multipath fading, path loss
guarantee convergence to a local or global optimum solution
  needs to be analyzed
rate of convergence
  faster than conventional and adaptive gradient-descent methods
  simulated for uniform and non-uniform weights on the samples
only simulated with fixed agent locations on 1-D and 2-D
robustness has not been considered
issue in simulation for moving agents

## Slide 6
Questions
existence of a solution
  given the number of agents, number of receivers, receiver locations, beam and null values, can the desired beam be formed?
resolve issue for the case of moving agents
integrate with node selection method
  alternate minimization approach
  select active agents: as it is
  iteratively update position of each agent : use IPG
  check if open-loop or not
simulate the working algorithm in phase-array toolbox
acceleration without a server and assuming peer-to-peer connected network of agents